## Slide 1: Parallel Computing with GPUs: Warp Level CUDA
Notes: 逻辑上，所有thread是并行的，但是，从硬件的角度来说，实际上并不是所有的thread能够在同一时刻执行，接下来我们将解释有关warp的一些本质。

## Slide 2: Thread Block Scheduling
Streaming Multiprocessor 1
Multiple blocks scheduled to Streaming Multiprocessor
Streaming Multiprocessor 2
warp是SM的基本执行单元。一个warp包含32个并行thread，这32个thread执行于SMIT模式。也就是说所有thread执行同一条指令，并且每个thread会使用各自的data执行该指令。

## Slide 3: Thread Block Scheduling
Thread Block 0
Thread Block 0, WARP 1
Thread Block 0, WARP 0
block可以是一维二维或者三维的，但是，从硬件角度看，
所有的thread都被组织成一维，每个thread都有个唯一的ID

## Slide 4: Warp Scheduling
Streaming Multiprocessor
Shared Memory / Cache
Scheduler / Dispatcher
Instruction Cache and Registers
一个warp中的线程必然在同一个block中，如果block所含线程数目不是warp大小的整数倍，那么多出的那些thread所在的warp中，会剩余一些inactive的thread。
Notes: Zero overhead to swap warps (warp scheduling)
  Warps contain only threads from a single
thread block
  Warps can be swapped with warps from different blocks assigned to the same streaming multi processor
  At any one time only one warp has operations being executed
    Memory movement happens in background
    也就是说，即使凑不够warp整数倍的thread，硬件也会为warp凑足，只不过那些thread是inactive状态，需要注意的是，即使这部分thread是inactive的，也会消耗SM资源。

## Slide 5: Warps and SIMD
GPU支持传统的控制流语句；
CPU有复杂的硬件设计可以很好的做分支预测；
GPU就没那么复杂的分支预测了
warp divergence问题只会发生在同一个warp中。
为了获得最好的性能，就需要避免同一个warp存在不同的执行路径。
Vector Unit
Instruction Pool
PU
Data Pool
PU
PU
PU
SIMD
Notes: Execution of GPU instructions is always in groups of threads called
warps
Within a warp execution on the hardware follows the SIMD execution model
  The view outside of a warp is SIMT
What happens if code within a warp has different control flow?
这样我们的问题就来了，因为所有同一个warp中的thread必须执行相同的指令，那么如果这些线程在遇到控制流语句时，如果进入不同的分支，那么同一时刻除了正在执行的分之外，其余分支都被阻塞了，十分影响性能。这类问题就是warp divergence。

## Slide 6: Coherent Code
Which is coherent?
Which is divergent?
global void b_kernel()
{
if (threadIdx.x % 2)
//something
else
//something else
}
global void a_kernel()
{
if (blockIdx.x % 2)
//something
else
//something else
}

## Slide 7: Divergence Example
Branch (divergence)
End of Branch (convergence)
global void a_kernel()
{
if (threadIdx.x % 2)
//something
else
//something else
}
if (threadIdx.x % 2)
else
All warps

## Slide 8: Divergence Example Alternative
Branch
End of Branch
global void a_kernel()
{
if (blockIdx.x % 2)
//something
else
//something else
}
if (blockIdx.x % 2)
Warp 0

## Slide 9: Divergence Example Alternative
Branch
End of Branch
global void a_kernel()
{
if (blockIdx.x % 2)
//something
else
//something else
}
else
Warp 1 (assuming thread block size of 32)

## Slide 10: Levels of divergence
global void a_kernel(int *a)
{
int a = a[threadIdx.x + blockIdx.x*blockDim.x] if (a==0)
//code for case 0
else if (a==1)
//code for case 1
else if (a==2)
//code for case 2 else if (a==3)
//code for case 3
}
global void a_kernel(int *a)
{
int a = a[threadIdx.x + blockIdx.x*blockDim.x] switch (a){
case(0):
//code for case 0 with break case(1):
//code for case 1 with break
case(2)
//code for case 2 with break
case(3)
//code for case 3 with break
}
}
Notes: Divergent code can be classified by how many “ways” it diverges.
  E.g. the following examples are 4-way divergent (and functionally equivalent)
If a warp has 32-way divergence this will have a massive impact on performance!

## Slide 11: 2D blocks and divergence
How many ways of divergence?
global void a_kernel()
{
if (threadIdx.y % 2)
//something
else
//something else
}
Thread Block 0
global void b_kernel()
{
if (threadIdx.y / 4)
//something else
//something else
}

## Slide 12: 2D blocks and divergence
How many ways of divergence?
3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Thread Block 0 – showing threadIdx.y
WARP 0
global void a_kernel()
{
if (threadIdx.y % 2)
//something
else
//something else
}
global void b_kernel()
{
if (threadIdx.y / 4)
//something else
//something else
}
2
0

## Slide 13: What is wrong with the following
global void max_kernel(int *a)
{
shared int max;
int my_local = a[threadIdx.x + blockIdx.x*blockDim.x];
if (my_local > max)
max = my_local;
}

## Slide 14
CUDA也存在互斥访问的问题：
global void max_kernel(int *a)
{
shared int max;
int my_local = a[threadIdx.x + blockIdx.x*blockDim.x];
if (my_local > max)
max = my_local;
}
Notes: 当一个线程改变变量,而另外一个线程在读取变量的值，执行原子操作类似于有一个自旋锁，只有等Ｘ的变量在改变完成之后，才能执行读操作，这样可以保证每一次读取的都是最新的值.

## Slide 15: 原子操作（Atomics）
global void max_kernel(int *a)
{
shared int max;
int my_local = a[threadIdx.x + blockIdx.x*blockDim.x];
if (my_local > max)
max = atomicMax(&max, my_local);
}
执行原子操作类似于有一个自旋锁，只有等变量在改变完成之后，才能执行读操作，这样可以保证每一次读取的都是最新的值.

## Slide 16: Histogramming
在统计学中，直方图（英语：Histogram）是一种对数据分布情况的图形表示，是一种二维统计图表，它的两个坐标分别是统计样本和该样本对应的某个属性的度量。
图像直方图（英语：Image Histogram）是用以表示数字图像中亮度分布的直方图，标绘了图像中每个亮度值的像素数。可以借助观察该直方图了解需要如何调整亮度分布。这种直方图中，横坐标的左侧为纯黑、较暗的区域，而右侧为较亮、纯白的区域。因此，一张较暗图片的图像直方图中的数据多集中于左侧和中间部分；而整体明亮、只有少量阴影的图像则相反。

## Slide 17: Histogramming
比如一个句子"Programming Massively Parallel Processors",我们构建一个字母出现频率的直方图.
A(4次), C(1), E(1), G(1), ...
Host端我们做统计的话,就会构建26大小的数组来表示a-z,然后遍历这个句子,碰到不同的case进行累加操作.
Device端并行化: 把这个sentense 划分成多个block,每个block统计自己的情况,同意保存到一个数组里面.

## Slide 18: CPU
#define SIZE (100*1024*1024)
int main(void) {
unsigned char *buffer =
(unsigned char*)big_random_block(SIZE);
clock_t start, stop; start = clock();
unsigned int histo[256];
for (int i = 0; i<256; i++)
histo[i] = 0;
for (int i = 0; i < SIZE; i++)
histo[buffer[i]]++; stop = clock();
float elapsedTime = (float)(stop - start) /
(float)CLOCKS_PER_SEC * 1000.0f;
printf("Time to generate: %3.1f ms\n", elapsedTime);
long histoCount = 0;
for (int i = 0; i<256; i++) { histoCount += histo[i]; }
printf("Histogram Sum: %ld\n", histoCount);
free(buffer); return 0;
}

## Slide 19: GPU 原子操作
__global__ void histo_kernel(unsigned char *buffer, long size, unsigned int *histo){
__shared__ unsigned int temp[256];
temp[threadIdx.x] = 0;
__syncthreads();
int i = threadIdx.x + blockIdx.x * blockDim.x;
int offset = blockDim.x *gridDim.x;
while (i<size){
atomicAdd(&temp[buffer[i]], 1);
i += offset;
}
__syncthreads();
atomicAdd(&(histo[threadIdx.x]), temp[threadIdx.x]);
}
__global__ void histo_kernel(unsigned char *buffer, long size, unsigned int *histo){
int i = threadIdx.x + blockIdx.x * blockDim.x;
int stride = blockDim.x * gridDim.x;
while (i < size){
atomicAdd(&histo[buffer[i]], 1);
i += stride;
}
}
GPU 原子操作+动态内存

## Slide 21
The two-phase parallel histogram algorithm.
Notes: In the first phase each CUDA thread block processes a region of the image and accumulates a corresponding local histogram, storing the local histogram in global memory at the end of the phase. The second kernel accumulates all per-block histograms into the final histogram stored in global memory. The work separation between blocks in the first phase reduces contention when accumulating values into the same bin.

## Slide 22
__global__ void histogram_gmem_atomics(const IN_TYPE *in, int width, int height, unsigned int *out)
{
// pixel coordinates
int x = blockIdx.x * blockDim.x + threadIdx.x;
int y = blockIdx.y * blockDim.y + threadIdx.y;
// grid dimensions
int nx = blockDim.x * gridDim.x;
int ny = blockDim.y * gridDim.y;
// linear thread index within 2D block
int t = threadIdx.x + threadIdx.y * blockDim.x;
// total threads in 2D block
int nt = blockDim.x * blockDim.y;
// linear block index within 2D grid
int g = blockIdx.x + blockIdx.y * gridDim.x;
// initialize temporary accumulation array in global memory
unsigned int *gmem = out + g * NUM_PARTS;
for (int i = t; i < 3 * NUM_BINS; i += nt) gmem[i] = 0;
// process pixels
// updates our block's partial histogram in global memory
for (int col = x; col < width; col += nx)
for (int row = y; row < height; row += ny) {
unsigned int r = (unsigned int)(256 * in[row * width + col].x);
unsigned int g = (unsigned int)(256 * in[row * width + col].y);
unsigned int b = (unsigned int)(256 * in[row * width + col].z);
atomicAdd(&gmem[NUM_BINS * 0 + r], 1);
atomicAdd(&gmem[NUM_BINS * 1 + g], 1);
atomicAdd(&gmem[NUM_BINS * 2 + b], 1);
}
}
global atomics

## Slide 23
shared atomics
__global__ void histogram_smem_atomics(const IN_TYPE *in, int width, int height, unsigned int *out)
{
// pixel coordinates
int x = blockIdx.x * blockDim.x + threadIdx.x;
int y = blockIdx.y * blockDim.y + threadIdx.y;
// grid dimensions
int nx = blockDim.x * gridDim.x;
int ny = blockDim.y * gridDim.y;
// linear thread index within 2D block
int t = threadIdx.x + threadIdx.y * blockDim.x;
// total threads in 2D block
int nt = blockDim.x * blockDim.y;
// linear block index within 2D grid
int g = blockIdx.x + blockIdx.y * gridDim.x;
// initialize temporary accumulation array in shared memory
__shared__ unsigned int smem[3 * NUM_BINS + 3];
for (int i = t; i < 3 * NUM_BINS + 3; i += nt) smem[i] = 0;
__syncthreads();
// process pixels
// updates our block's partial histogram in shared memory
for (int col = x; col < width; col += nx)
for (int row = y; row < height; row += ny) {
unsigned int r = (unsigned int)(256 * in[row * width + col].x);
unsigned int g = (unsigned int)(256 * in[row * width + col].y);
unsigned int b = (unsigned int)(256 * in[row * width + col].z);
atomicAdd(&smem[NUM_BINS * 0 + r + 0], 1);
atomicAdd(&smem[NUM_BINS * 1 + g + 1], 1);
atomicAdd(&smem[NUM_BINS * 2 + b + 2], 1);
}
__syncthreads();
// write partial histogram into the global memory
out += g * NUM_PARTS;
for (int i = t; i < NUM_BINS; i += nt) {
out[i + NUM_BINS * 0] = smem[i + NUM_BINS * 0];
out[i + NUM_BINS * 1] = smem[i + NUM_BINS * 1 + 1];
out[i + NUM_BINS * 2] = smem[i + NUM_BINS * 2 + 2];
}
}

## Slide 24: second kernel： we accumulate all partial histograms into the global one
__global__ void histogram_final_accum(const unsigned int *in, int n, unsigned int *out)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < 3 * NUM_BINS) {
unsigned int total = 0;
for (int j = 0; j < n; j++)
total += in[i + NUM_PARTS * j];
out[i] = total;
}
}

## Slide 25
Performance of our histogram algorithm comparing global memory atomics to shared memory atomics on a Kepler architecture NVIDIA GeForce GTX TITAN GPU.

## Slide 26
Performance of our histogram algorithm comparing global memory atomics to shared memory atomics on a Maxwell architecture NVIDIA GeForce GTX TITAN X GPU.